## Slide 1: Background on GSM Networks
GSM is a 2G digital cellular network
  Replaced AMPS analog network ~1991
  Initially offered only Circuit Switched voice and SMS
    Packet Switching was added via GPRS ~2001
  Utilizes Time Division Multiple Access (TDMA) multiplexing

## Slide 2: GSM Infrastructure
Access Network
User Equipment (UE)
Base Transceiver Station (BTS)
Base Station Controller (BSC)
Master System Controller (MSC)
Home Location Register (HLR)
Circuit Switched Core Network
Minimum System Hardware Required:

## Slide 3: Radio Access Network Details
Each BTS contains some fixed number of Transmit and Receive (TRX) channels
  Each is configured for a specific ARFCN (Absolute Radio Frequency Channel Number)
  4 Common frequency bands
    GSM 900 (Europe, Asia, Middle East)
    GSM 850 (Americas)
    DCS 1800 (Europe, Asia, Middle East)
    PCS 1900 (Americas)

## Slide 4: Radio Access Network Details
Each TRX module offers one Downlink & Uplink
  Frequency offset between them depends on band
  200 KHz channel bandwidth
TDMA provides 8 full-rate time slots per frame
  Possibility of 16 half-rate
  Minimum of 1-2 slots required for control signaling
  Exact frame configuration up to carrier
CCH
CCH
FR-TCH
FR-TCH
FR-TCH
FR-TCH
FR-TCH
FR-TCH

## Slide 5: Radio Access Network Details
Consequence of TDMA frame size is limited maximum users
  Depending on configuration, maximum of 12-14
  Once all slots on a TRX are taken, no new calls can be established
Most BTSs/Base Stations offer many TRXs to reduce conflict
  Frequency deconfliction is necessary
CCH
CCH
User 1
User 2
User 3
User 4
User 5
User 6
User 7
User 8
User 9
User 10
User 11
User 12
User 13